## Slide 2: Interpolation of loudspeaker level balloons from polar measurements by using deep learning
Víctor Manuel Catalá Iborra1
1 DAS AUDIO GROUP, Fuente del Jarro, Spain

## Slide 3
Polar diagrams.
Motivation

## Slide 4
Horizontal (red) and vertical (blue) polar measurement points.
Motivation

## Slide 5: Motivation
Loudspeaker radiation balloon (level and phase)
Notes: Design, design verification, loudspeaker models for simulation software

## Slide 6
Polar system coordinates per AES, 2008 (reaffirmed 2014).
Motivation

## Slide 7
2664 measurement points which means 82584 SPL values with 1/3 oct resolution
Motivation

## Slide 8
3D acquisition system with 2 turntables.
Motivation

## Slide 9
Measurement set-up at DAS Audio Auditorium.
Motivation
Notes: 2 turntables, big enough to allow window techniques down to 160Hz, low RT, low noise. Not available for other pourposes while measuring and setup

## Slide 10
Loudspeaker radiation balloon (level and phase)
Motivation

## Slide 11: Method
Traditional interpolation methods are based on the data of the loudspeaker being analyzed
Neural networks allow us to take profit of many loudspeaker data to build a model and then, apply it to a specific loudspeaker.

## Slide 12
The problem is reduced to an incomplete-image recovery problem
Method

## Slide 13
Method
Proposed U-net architecture

## Slide 14
Layer Input size Stride Padding Kernel size Output size
conv2d_44 (2664, 44, 1) (2, 1) valid (75, 3) (1295, 42, 16)
conv2d_45 (1295, 42, 16) (2, 2) valid (75, 3) (611, 20, 32)
conv2d_46 (611, 20, 32) (2, 2) valid (75, 3) (269, 9, 64)
conv2d_47 (269, 9, 64) (2, 2) valid (75, 3) (98, 4, 128)
conv2d_48 (98, 4, 128) (2, 2) valid (75, 3) (12, 1, 256)
conv2d_transpose_32 (12, 1, 256) (2, 1) valid (76, 4) (98, 4, 128)
conv2d_transpose_33 (98, 4, 256) (2, 2) valid (75, 3) (269, 9, 64)
conv2d_transpose_34 (269, 9, 128) (2, 2) valid (75, 4) (611, 20, 32)
conv2d_transpose_35 (611, 20, 64) (2, 2) valid (75, 4) (1295, 42, 16)
conv2d_transpose_36 (1295, 42, 32) (2, 1) valid (76, 3) (2664, 44, 16)
conv2d_49 (2664, 44, 17) NA same (75, 4) (2664, 44, 1)
Parameters of the proposed U-net.
Method

## Slide 15: Results
Training data images 1-2-3. Left column: only polar data. Central column: ground truth. Right: U-net prediction

## Slide 16
Results
Training data images 4-5. Left column: only polar data. Central column: ground truth. Right: U-net prediction

## Slide 17
Results
Validation data. Left column: only polar data. Central column: ground truth. Right: U-net prediction

## Slide 18
Results
Test data. Left column: only polar data. Central column: ground truth. Right: U-net prediction

## Slide 19
 | Mean Absolute Error (MAE)
Training data | 2.8 dB
Validation data | 4.0 dB
Test data | 3.8 dB
Results

## Slide 20
Polar plot at Phi=45º - 250 Hz
Polar plot at Phi=45º - 500 Hz
Results

## Slide 21
Polar plot at Phi=45º - 1 kHz
Polar plot at Phi=45º - 2 kHz
Results

## Slide 22
Polar plot at Phi=45º - 4 kHz
Polar plot at Phi=45º - 8 kHz
Results

## Slide 23
Polar plot at Phi=45º - 16 kHz
Results

## Slide 24: Conclusions and further research
Neural Networks can be used to approximate level loudspeaker radiation balloons from polar measurements. In particular, U-net deep learning architectures can provide MAE lower that 4 dB over full balloons.
At high frequencies, with steeper variation of SPL against angles, the performance of the proposed network is lower. Refined architectures, more data and farther research are needed to improve accuracy.
Similar methods could be applied to phase interpolation in order to get complex responses.
More powerful models could be achieved by combining true polar measurements and full 3D simulations (from Finite Element Method software, for example) as input data, to obtain more accurate predictions. In this case, simple polar measurements would refine full 3D simulations.

## Slide 25: Thanks!